Tutorial 5
LNGANG002, BTJMAL001
17 October 2021

Question 1
Microcontrollers have a fixed hardware structure, unlike FPGAs, which can be reconfigured as needed by the user. FPGAs by default have operate in a highly parallel manner as opposed to single-core microcontrollers, that must switch between processes to simulate synchronous operation.

FPGA Advantages

1. Very fast and efficient paralell computing
2. Can be reprogrammed to perform whatever function is required.

FPGA Disadvantages

1. Expensive
2. Higher power consumption

Question 2

Blocking assignments mean that each command is evaluated in-order, 1 after the other. Each assignment is evaluated and then updated before the next is evaluated. All the assignments will occur on the same clock edge.
In a non-blocking assignment, the statements afterwards are allowed to continue. Each statement’s RHS is evaluated, and then all LHSs are assigned together.

For example, the blocking code snippet will execute as expected, with q2 becoming the value of q1 after q1 has become the value of in.
In the non-blocking snippet, q1 and q2 wil first be evaluated, then assigned. Q2 will take on the value of q1 that existed before the q1 = in statement was executed.

Question 3

By order output
“0	1	10”

By name output
“0	1	01”

In the By-order output, the value of A is passed into the clk value for the module, and the clk value is instead used as the value of A leading to an unexpected value of 1 + 0 = 2. When mapping by name, the correct values were used, leading to the expected outputs.

Both methods have advantages and disadvantages. Generally for a small number of inputs, mapping by order is preferred. For a large number, the chances of making an ordering mistake is increased, so mapping by name is preferred.
Mapping by name does however increase code clutter and can make sections of the code difficult to understand.